## Slide 1: IVcache: Defending Cache Side Channel Attacks via Invisible Accesses
Yanan Guo, Andrew Zigerelli, Youtao Zhang, and Jun Yang

## Slide 2: Cache Side-channel Attacks
The shared hardware platform can be used to leak information
With a shared LLC, the attacker can observe a victim’s cache access
  Can cross VM boundries
  Hard to be detected
Shared LLC
L1
L1
L1
L1
Victim
Attacker
Requires data sharing | No data sharing
Flush+Reload | Prime+Probe
Evict+Reload | Probablistic Prime+Probe
Coherence Attack | LRU Attack

## Slide 3: Cache Side-channel Attacks
The shared hardware platform can be used to leak information
With a shared LLC, the attacker can observe a victim’s cache access
  Can cross VM boundries
  Hard to be detected
Shared LLC
L1
L1
L1
L1
Victim
Attacker
Requires data sharing | No data sharing
Flush+Reload | Prime+Probe
Evict+Reload | Probablistic Prime+Probe
Coherence Attack | LRU Attack

## Slide 4: IVcache: The Big Picture
Cache Access
Cache State Changes
Block Path 1
Block Path 2
Secure Cache Design
Hard to identify the attacker
Overhead on every user
Problem
Classify processes into domains
Identify accesses from security-sensitive domains
Make those accesses strictly invisible to other domains
Negligible overhead on security-sensitive domains, no overhead on others
IVcache

## Slide 5: How to make the victim's access invisible?

## Slide 6: Prime+Probe Attack
Step 1: Attacker brings his cache lines into the target set
Private Cache
Shared Cache
Victim
Attacker
Cache line
Cache set

## Slide 7: Prime+Probe Attack
Step 1: Attacker brings his cache lines into the target set
Private Cache
Shared Cache
Victim
Attacker

## Slide 8: Prime+Probe Attack
Step 2: Attacker waits for the victim's behavior
Private Cache
Shared Cache
Victim
Attacker

## Slide 9: Prime+Probe Attack
Step 2: Attacker waits for the victim's behavior
Private Cache
Shared Cache
Victim
Attacker

## Slide 10: Prime+Probe Attack
Step 3: Attacker accesses the probe set and determines was any line evicted
Private Cache
Shared Cache
Victim
Attacker

## Slide 11: Prime+Probe Attack
Step 3: Attacker accesses the probe set and determines is any line evicted
Private Cache
Shared Cache
Victim
Attacker

## Slide 12: Make the Victim Invisible
What is visible to the attacker?
  Whether all the attacker's cache lines are still in LLC.
What is causing the change on these cache lines?
  The LLC eviction caused by the victim's LLC miss.
IVcache solution?
  For victim's LLC misses, avoid cache eviction on other domains' lines!

## Slide 13: IVcache-Prime+Probe
Case 1: the target LLC set has vancacy for a new line
Private Cache
Shared Cache
Victim
Attacker

## Slide 14: IVcache-Prime+Probe
Case 1: the target LLC set has space
Private Cache
Shared Cache
Victim
Attacker
Load the data from memory and fill it in LLC as normal

## Slide 15: IVcache-Prime+Probe
Case 2: the target LLC set is full
Private Cache
Shared Cache
Victim
Attacker

## Slide 16: IVcache-Prime+Probe
Case 2: the target LLC set is full
Private Cache
Shared Cache
Victim
Attacker
Eviction target
Try to perform self-eviction

## Slide 17: IVcache-Prime+Probe
Case 2: the target LLC set is full
Private Cache
Shared Cache
Victim
Attacker
If cannot performe self-eviction, bypass the cache hierarchy

## Slide 18: IVcache-Design Summary
Problem 1: Prime+Probe attack
Solution 1: Avoid visible LLC state changes caused by victim's LLC misses
Implementation 1: Self-eviction+Bypass cache
Problem 2: LRU attack
Solution 2: Avoid visible LLC state changes caused by victim's LLC hits
Implementation 2: RLRU replacement policy

## Slide 19: LRU Attack
Private Cache
Shared Cache
Victim
Attacker
Step 1: Attacker fills the set but leaves the victim's line in LLC

## Slide 20: LRU Attack
Step 1: Attacker fills the set but leaves the victim's line in LLC
11
10
9
8
7
6
5
4
3
2
1
Private Cache
Shared Cache
Victim
Attacker
Least Recent Used Line

## Slide 21: LRU Attack
Step 2: Attacker waits for the victim's behavior
11
10
9
8
7
6
5
4
3
2
1
Private Cache
Shared Cache
Victim
Attacker
Most Recent Used Line
Least Recent Used Line

## Slide 22: LRU Attack
Step 3: Attacker brings a new line and evicts the LRU line
11
10
9
8
7
6
5
4
3
2
1
Private Cache
Shared Cache
Victim
Attacker
12

## Slide 23: LRU Attack
Step 4: Attacker accesses all the previous lines to determine the LRU line that was evicted
12
11
10
9
8
7
6
5
4
3
2
1
Private Cache
Shared Cache
Victim
Attacker

## Slide 24: LRU Attack
Step 4: Attacker accesses all the previous lines to determine the LRU line that was evicted
11
10
9
8
7
6
5
4
3
2
12
Private Cache
Shared Cache
Victim
Attacker

## Slide 25: Make the Victim Invisible
What is visible to the attacker?
  Whether all the attacker's cache line are still in LLC.
What is causing thechange to the attacker's lines?
  The changed LRU state caused by the victim's LLC hit.
IVcache solution?
  For victim's LLC hits, avoid visible LRU state changes!

## Slide 26: IVcache-LRU attack
Naïve solution: random replacement
  Significant performance overhead
Solution: RLRU Replacement Policy
LLC set
Random
Replacement
LRU
Tacking
Inactive Group
Active Group
RLRU cache behavior
  Non-victim's accesses are treated as normal
  Pin the victim's lines in inactive group

## Slide 27: IVcache-Design Summary
Problem 1: Prime+Probe attack
Solution 1: Avoid visible LLC state changes caused by victim's LLC misses
Implementation 1: Self-eviction+Bypass cache
Problem 2: LRU attack
Solution 2: Avoid visible LLC state changes caused by victim's LLC hits
Implementation 2: RLRU replacement policy

## Slide 28: IVcache-Design Summary
Problem 1: Prime+Probe attack
Solution 1: Avoid visible LLC state changes caused by victim's LLC misses
Implementation 1: Self-eviction+Bypass cache
Problem 2: LRU attack
Solution 2: Avoid visible LLC state changes caused by victim's LLC hits
Implementation 2: RLRU replacement policy
Perfomance Degradation!

## Slide 29: IVcache-Optimization1
Problem 1: Self-eviction and Bypass can reduce L1 hit rate by 30%-80%
Solution 1: Relax cache inclusion (Fill L1 cache wihle bypassing LLC)
(When bypassing LLC, fill L1 with a read-only copy and record in Record Buffer)
RO
Private Cache
Shared Cache
Victim
Attacker
Read hits!

## Slide 30: IVcache-Optimization1
Problem 1: Self-eviction and Bypass can reduce L1 hit rate by 30%-80%
Solution 1: Relax cache inclusion (Fill L1 cache wihle bypassing LLC)
(When bypassing LLC, fill L1 with a read-only copy and record in Record Buffer)
RO
Private Cache
Shared Cache
Victim
Attacker
Write misses!

## Slide 31: IVcache-Optimization1
Problem 1: Self-eviction and Bypass can reduce L1 hit rate by 30%-80%
Solution 1: Relax cache inclusion (Fill L1 cache wihle bypassing LLC)
(When bypassing LLC, fill L1 with a read-only copy and record in Record Buffer)
Private Cache
Shared Cache
Victim
Attacker
Invalidate the L1 copy!

## Slide 32: IVcache-Optimization2
Optimization1 is not enough for performance, why?
    It only benefits read accesses
    Write accesses will still starve in cache
Cache is a reactive architecture
    Cache only reacts to CPU’s requirement
    Cache does not actively evict data
Solution: Active LLC invalidation
  Actively invalidate a line from the inactive group in an LLC set every once a while