## Slide 1: Leaky Way: A Conflict-Based Cache Covert Channel Bypassing Set Associativity
Yanan Guo, Xin Xin, Youtao Zhang, Jun Yang
University of Pittsburgh

## Slide 2: Cache Attacks

## Slide 3: Conflict-Based Cache Attacks
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
Critical step: build cache conflicts to evict the victim’s data.
  Prime+Probe, Prime+Scope, Evict+Reload…: requires priming the cache set.

## Slide 4: Conflict-Based Cache Attacks
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
Critical step: build cache conflicts to evict the victim’s data.
  Prime+Probe, Prime+Scope, Evict+Reload…: requires priming the cache set.

## Slide 5: Conflict-Based Cache Attacks
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A2
Critical step: build cache conflicts to evict the victim’s data.
  Prime+Probe, Prime+Scope, Evict+Reload…: requires priming the cache set.

## Slide 6: Conflict-Based Cache Attacks
V
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A3
A2
Critical step: build cache conflicts to evict the victim’s data.
  Prime+Probe, Prime+Scope, Evict+Reload…: requires priming the cache set.

## Slide 7: Conflict-Based Cache Attacks
A4
Set 0
Set 1
Set n
…
Way 0
Way 1
Way 2
Way 3
A1
A3
A2
Set conflicts
Priming the set
Critical step: build cache conflicts to evict the victim’s data.
  Prime+Probe, Prime+Scope, Evict+Reload…: requires priming the cache set.

## Slide 8
Can we build set conflicts without priming the set?

## Slide 9: Non-Temporal Prefetch
x86 data prefetching instructions
  PREFETCHT0, PREFETCHT1…, regular prefetch instructions.
  PREFETCHNTA…, prefetch instruction for non-temporal data.
PrefetchNTA brings data into the L1 cache and the LLC/Snoop Filter.

## Slide 10: Non-Temporal Prefetch
x86 data prefetching instructions
  PREFETCHT0, PREFETCHT1…, regular prefetch instructions.
  PREFETCHNTA…, prefetch instruction for non-temporal data.
PrefetchNTA brings data into the L1 cache and the LLC/Snoop Filter.
“For PrefetchNTA, the fill into the L3 cache or Snoop Filter may not be placed into the Most Recent Used Positioned and may be chosen for replacement faster than a regular cache fill”

## Slide 11
How is this implemented in hardware
…especially with inclusive LLCs

## Slide 12: Intel Inclusive-LLC Policy
From prior reverse-engineering result: Quad-age LRU (0-3)
  Oldest age = 3, youngest age = 0
Insertion Policy
  When filled into the LLC, age = 2

## Slide 13: Intel Inclusive-LLC Policy
From prior reverse-engineering result: Quad-age LRU (0-3)
  Oldest age = 3, youngest age = 0
Insertion Policy
  When filled into the LLC, age = 2
Replacement Policy
  Evicts the first line with age 3
  If not exist, increase every line’s age

## Slide 14: Intel Inclusive-LLC Policy
From prior reverse-engineering result: Quad-age LRU (0-3)
  Oldest age = 3, youngest age = 0
Insertion Policy
  When filled into the LLC, age = 2
Replacement Policy
  Evicts the first line with age 3
  If not exist, increase every line’s age
Updating Policy
  Upon a cache hit, age = age - 1

## Slide 15: Intel Inclusive-LLC Policy
From prior reverse-engineering result: Quad-age LRU (0-3)
  Oldest age = 3, youngest age = 0
Insertion Policy
  When filled into the LLC, age = 2
Replacement Policy
  Evicts the first line with age 3
  If not exist, increase every line’s age
Updating Policy
  Upon a cache hit, age = age - 1

## Slide 16: PrefetchNTA Reverse Engineering
Observation 1: LLC treats prefetched data differently than loaded data.
Insertion Policy
  When filled into the LLC, age = 2
Updating Policy
  Upon a cache hit, age = age - 1
Insertion Policy
  When filled into the LLC, age = 3
Updating Policy
  Upon a cache hit, age = age
Load
PrefetchNTA
VS

## Slide 17: PrefetchNTA Reverse Engineering
Observation 2: The execution time of PrefetchNTA is related to the location of the target data.

## Slide 18
What do these observations give us?

## Slide 19: Cache Conflicts Bypassing Associativity
PrefetchNTA
  Insertion Policy
    When filled into the LLC, age = 3
  Updating Policy
    Upon a cache hit, age = age - 1
Observation 1
Age

## Slide 20: Cache Conflicts Bypassing Associativity
PrefetchNTA
  Insertion Policy
    When filled into the LLC, age = 3
  Updating Policy
    Upon a cache hit, age = age - 1
Observation 1

## Slide 21: Cache Conflicts Bypassing Associativity
PrefetchNTA
  Insertion Policy
    When filled into the LLC, age = 3
  Updating Policy
    Upon a cache hit, age = age - 1
Observation 1

## Slide 22: Cache Conflicts Bypassing Associativity
Eviction candidate

## Slide 23: Cache Conflicts Bypassing Associativity
Prefetch d0
Eviction candidate

## Slide 24: Cache Conflicts Bypassing Associativity
Eviction candidate
Prefetch d1

## Slide 25: Cache Conflicts Bypassing Associativity
Eviction candidate
Prefetch d0

## Slide 26: Covert Channel Based on PrefetchNTA
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.

## Slide 27: Covert Channel Based on PrefetchNTA
Send “1”
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.

## Slide 28: Covert Channel Based on PrefetchNTA
Send “1”
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.

## Slide 29: Covert Channel Based on PrefetchNTA
Get the bit
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.
LLC miss!

## Slide 30: Covert Channel Based on PrefetchNTA
Get the bit
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.

## Slide 31: Covert Channel Based on PrefetchNTA
Send “0”
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.

## Slide 32: Covert Channel Based on PrefetchNTA
Get the bit
Sender:
  Prefetch sender’s data ds to send “1”.
  Not prefetch to send “0”.
Receiver:
  Prefetch receiver’s data dr and time the prefetch.
  If hit in the LLC: received “0”.
  If miss in the LLC: received “1”.
LLC hit!

## Slide 33: Covert Channel Based on PrefetchNTA
Prior conflict-based covert channels require priming the set
  Prime+Probe, Eivct+Reload, Prime+Scope…
  This makes conflict-based covert channels slow.

## Slide 34
What about side channel attacks?

## Slide 35: PrefetchNTA with Side Channel Attacks
The proposed covert channel is unlikely a side channel
  We can only leak the victim’s prefetch pattern.
PrefetchNTA makes it easier to manipulate replacement states
  We can use it to improve attacks based on replacement states!
  E.g., Prime+Scope, 192 cache references to 33 cache references

## Slide 36: PrefetchNTA with Prime+Scope
Prime+Scope: a high resolution cache attack
  Key conditions in Prime+Scope
    The attacker knows the eviction candidate of the target LLC set after priming.
    This eviction candidate is present in the attacker’s L1 after priming.
192 cache references
33 cache references
Prime stage:
1906 cycles
VS
1043 cycles

## Slide 37: More in the Paper
PrefetchNTA with other side channel attacks.
Faster eviction set construction algorithm with PrefetchNTA.
PrefetchNTA with non-inclusive LLCs.
Potential defense methods against prefetch-based attacks.

## Slide 38: Summary
Reverse Engineering PrefetchNTA
Faster Eviction Set Construction
A New Covert Channel
Improved Cache Side Channels

## Slide 39
Leaky Way: A Conflict-Based Cache Covert Channel Bypassing Set Associativity
Yanan Guo, Xin Xin, Youtao Zhang, Jun Yang
University of Pittsburgh
Artifacts: https://github.com/PittECEArch/LeakyWay